## Slide 1
Wireless UHF RFID based bladder pressure sensor
1
Laboratorio
Elettromagnetismo
Pervasivo
Sistemi Wearable e Telemetria Medica
A.A 2024-25
(Final course project)
Prof. G. Marrocco
Tutor: Ing. Francesca Nanni
TASK 6

## Slide 2: Approaching the final design
Adding chip footprint and matching the impedance
(@915 MHz)= 30 - i195Ω
Simulations
Real bladder
Bladder as a balloon

## Slide 3: Final Model Dimension
Dipole L = 27mm x W = 1.5 mm
Elliptical Incapsulation:
-Major axis 30 mm
-Minor axis 15 mm
Asygn AS3213S_5 Footprint
Elliptical Incapsulation:
-Bottom silicon layer 1 mm
-Top low-ε material 2 mm

## Slide 4: Real Bladder Tag Impedance
Including chip footprint
Half-Filled bladder
Empty bladder
Full bladder
No variations with filling condition (as we already knew)

## Slide 5: Schematic model
82nH inductor
Ideally we would need an 89 nH series inductor to match chip's impedance
According to available real inductors, 82 nH showed best performances
Reader Antenna

## Slide 6: Real bladder τ
50% air and 50% urine

## Slide 7: Real bladder GT
50% air and 50% urine
Nothing changes between the three types of filling (empty, 50/50, full), therefore fluid in the bladder is not a determining factor.

## Slide 8: Balloon's dielectric characteristics
Balloon thickness considered= 0,1 mm
Cole – Cole model for latex
Results:
ε = 15
σ = 0,5
"Characterisation of the dielectric properties of rubber latex from 0.5 to 33 GHz"
Equation models the complex permittivity ε* as the sum of two dielectric relaxations and a conductivity term, where ε∞,d, Δε1, and Δε2 depend on the dry rubber content (DRC), σd depends on both temperature and DRC, and ε0,space is the permittivity of free space.
Used fluid: saline solution  ε= 72, σ = 1,5 (Very similar to the one used until now)

## Slide 9: Bladder as balloon τ
50% air and 50% urine
We ran all the simulations using always the same 82 nH inductor

## Slide 10: Bladder as balloon GT
50% air and 50% urine

## Slide 11: Bladder as balloon τ
Full
With half and full filling conditions the impedance matching still reaches good values

## Slide 12: Bladder as balloon GT
Full

## Slide 13: Bladder as balloon τ
Empty
Due to the thin layer of the balloon, the tag will sense the content of the "bladder". For empty configuration there is a big change in impedance

## Slide 14: Bladder as balloon GT
Empty
Despite the matching worsening, a Gt = -35 dB should still be enough to communicate

## Slide 15: Conclusions
The simulated prototype showed good performances in almost all the cases, also considering a thin balloon instead of a realistic bladder.
82 nH Inductor can match the tag impedance for full and half filled bladder
Even in the worst case (empty bladder), the transducer gain should be high enough to close the communication link
Now it's time for prototyping...